HX200 - BUC Information from Specifications

(How to calculate the BUC Value)

Gain  ______________     Power Output _________________

___________________________________________________________________

Cable Information - (Total cable distance *db loss/ft) (i.e. 100 ft x 0.62 db/ft + -6.2)

IFL Attenuation Value  _____________________

___________________________________________________________________

Calculating Attenuation Value

Step 1

Subtract the Power output of the BUC from the Gain at the BUC

i.e. +56db less +36db = -20db

Calculated BUC Value  _____________

Step 2

Subtract the IFL Attenuation value (-6.2db) from Calculated BUC Value (-20db)

i.e. +20db less -6.2db = -13.8db

Calculated BUC Value  _____________

___________________________________________________________________

Net Attenuation Value to be entered into IDU    ________________