# Text boxes

Satellite Antenna Roof Mount & Dish-Antenna

Antenna Specifications

--------------------------------------------------------------------------------------------------------

Frequency Range			12.2 to 12.7 GHz

Polarization			RHCP/ LHCP

Reflector F/D			0.6

Reflector Material			Galvanized Sheet Steel/ Power Coat Paint

Antenna Mount Components Material	Galvanized Sheet Steel/ Power Coat Paint

Hardware Material			Steel w/ Zinc + Clear Chromate + Clear Top Coat

Antenna				Antenna Gain       34dB

LNB Noise Figure			1.1 Max

Output Frequency			950 to 1450 MHz

LNB Conversation Gain Range	50 to 62dB

Operating Temperature		-34 to +52 C(-29.2 to 125.6 F)

Wind Loading			Operational          50mph

Survival               100 mph

Gross Weight    10 lbs

18” DBS Antenna and Dual Output LNBF

Model 6218

The system consists of the following Components:

` 18” Steel Antenna	 ` Assembly Hardware

` Universal Mast/ Base Assembly	 ` (1) Dual LNBF

` Bracket and Arm Assembly	 ` Instruction Sheet

Our non-penetrating roof mounts have been specifically designed for our line of offset reflectors. Mechanically tested and field proven, these fully adjustable mounts meet the performance requirements of Demanding commercial applications. The non-penetrating roof mount is designed to be used on a flat roof and has provisions for concrete block ballast.  The mount components are powder coated, pre-galvanized steel.  All hardware is plated for excellent corrosion resistance.

• It includes rubber roof pads

• Tray type mount. Use cored or solid blocks.

The mount components are powder-coated,

pre-galvanized steel.

Non-Penetrating Roof Mount

• UPS shippable single carton packaging.

• Pre-assembled base.

Roof Mount Specifications

This non-penetrating roof mount has a 2.38” (60 mm) O.D. mast and a 36” x 36” base, which is designed for the 75 cm antenna. This model can also be used with 90 cm and 1.0 m antennas with a “hybrid” 2.38” (60 mm) Az/El cap when higher wind loads are not expected.

Maximum Antenna Wind Loading

75 cm        106 mi/h

90 cm          89 mi/h

1.0 m           80 mi/h