| Satellite | IA8 |
| --- | --- |
| Transponder Name | 10K* | 11K | 19K | 20K | 22K | 23K |
| Channel ID | 45 | 44 | 46 | 43 | 41 | 42 |
| Frequency in MHz | 1150 | 1170 | 1330 | 1350 | 1390 | 1410 |
| Longitude in Degrees | 89 | 89 | 89 | 89 | 89 | 89 |
| Hemisphere | West | West | West | West | West | West |
| Receive Polarization | H | V | V | H | H | V |
| Transmit Polarization | V | H | H | H | H | H |
| Offset | 0 | 0 | 0 | 0 | 0 | 0 |
| Symbol Rate (Msps) | 30 | 30 | 30 | 30 | 30 | 30 |
| Modulation Type | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK |
| Viterbi Mode | 7/8 | 7/8 | 7/8 | 7/8 | 7/8 | 7/8 |
| Shadow States | PR and most of Canada | PR and most of Canada | PR and most of Canada | PR and most of Canada | PR and most of Canada | PR and most of Canada |
| Date Available | 11/15/05 | 10/21/05 | 01/05/06 | 9/30/05 | 8/25/05 | 8/30/05 |
| Isolation | 30 | 30 | 30 | 30 | 30 | 30 |
| ACP | 60 | 60 | 60 | 60 | 60 | 60 |
| Minimum Signal | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 |

*Note: The IA8-10K will only be used for commissioning the DW7000.

| Satellite | AMC3 |
| --- | --- |
| Transponder Name | 5K | 6K | 10K | 15K | 17K |
| Channel ID | 30 | 29 | 27 | 28 | 26 |
| Frequency in MHz | 1050 | 1070 | 1150 | 1250 | 1290 |
| Longitude in Degrees | 87 | 87 | 87 | 87 | 87 |
| Hemisphere | West | West | West | West | West |
| Receive Polarization | H | V | V | H | H |
| Transmit Polarization | H | H | H | H | H |
| Offset | 0 | 0 | 0 | 0 | 0 |
| Symbol Rate (Msps) | 30 | 10 | 30 | 30 | 30 |
| Modulation Type | QPSK | QPSK | QPSK | QPSK | QPSK |
| Viterbi Mode | 5/6 | 3/4 | 2/3 | 7/8 | 7/8 |
| Shadow States | FL, MI, MN, MT, ND, SD, PR & VI | FL, MI, MN, MT, ND, SD, PR & VI | FL, MI, MN, MT, ND, SD, PR & VI | FL, MI, MN, MT, ND, SD, PR & VI | FL, MI, MN, MT, ND, SD, PR & VI |
| Date Available | 11/24/04 | Live | Live | Live | Live |
| Isolation | 30 | 30 | 30 | 30 | 30 |
| ACP | 66 | 66 | 66 | 66 | 66 |
| Minimum Signal | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 |
| Framing Mode | HDLC | HDLC | HDLC | HDLC | HDLC |

| Satellite | G11 |
| --- | --- |
| Transponder Name | 2K | 5K | 20K | 21K | 23K |
| Channel ID | 2 | 31 | 6 | 3 | 1 |
| Frequency in MHz | 990 | 1050 | 1350 | 1370 | 1410 |
| Longitude in Degrees | 91 | 91 | 91 | 91 | 91 |
| Hemisphere | West | West | West | West | West |
| Receive Polarization | V | H | V | H | H |
| Transmit Polarization | H | V | H | H | H |
| Offset | 0 | 0 | 0 | 0 | 0 |
| Symbol Rate (Msps) | 30 | 10 | 30 | 30 | 30 |
| Modulation Type | QPSK | QPSK | QPSK | QPSK | QPSK |
| Viterbi Mode | 7/8 | 5/6 | 3/4 | 5/6 | 2/3 |
| Shadow States | AL, AR, AZ, CA, CO, FL, GA, KS, LA, MN, MS, TX |  |  |  |  |
| Date Available | Live | Live | Live | Live | Live |
| Isolation | 32 | 32 | 32 | 32 | 32 |
| ACP | 66 | 66 | 66 | 66 | 66 |
| Minimum Signal | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 |
| Framing Mode | HDLC | HDLC | HDLC | HDLC | HDLC |
| To find out how to check frequency, go to HNS-24381 | Go To Top |  |

| Satellite | SatMex5 |
| --- | --- |
| Transponder Name | 1k | 2k | 5k | 6k | 7k | 9k | 11k | 14k | 15k | 16k |
| Channel ID | 19 | 8 | 17 | 7 | 15 | 16 | 32 | 18 | 4 | 20 |
| Frequency in MHz | 970 | 990 | 1050 | 1070 | 1090 | 1130 | 1170 | 1230 | 1250 | 1270 |
| Longitude in Degrees | 117 | 117 | 117 | 117 | 117 | 117 | 117 | 117 | 117 | 117 |
| Hemisphere | W | W | W | W | W | W | W | W | W | W |
| Receive Polarization | H | V | H | V | H | H | H | V | H | V |
| Transmit Polarization | H | H | H | H | H | H | H | H | H | H |
| Offset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Symbol Rate (Msps) | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 |
| Modulation Type | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK |
| Viterbi Mode | 7/8 | 7/8 | 7/8 | 7/8 | 7/8 | 7/8 | 7/8 | 7/8 | 7/8 | 7/8 |
| Shadow States | MN, ND, WA, MT, ID |  | MN, ND, WA, MT, ID |  | MN, ND, WA, MT, ID, and Puerto Rico | MN, ND, WA, MT, and ID |  |  |  | MN, ND, WA, MT, ID |
| Date Available | Live | Live | Live | Live | Live | Live | Live | Live | Live | Live |
| Isolation | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 |
| ACP | 81 | 81 | 81 | 81 | 81 | 81 | 81 | 81 | 81 | 81 |
| Minimum Signal | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 |
| Framing Mode | HDLC | HDLC | HDLC | HDLC | HDLC | HDLC | HDLC | HDLC | HDLC | HDLC |
| To find out how to check frequency go to HNS-24381 | Go To Top |

| Satellite | G4R |
| --- | --- |
| Transponder Name | 1K | 3K | 8K | 14K | 15K | 20K | 21K |
| Channel ID | 13 | 5 | 9 | 14 | 10 | 11 | 12 |
| Frequency in Mhz | 970 | 1018 | 1110 | 1230 | 1250 | 1350 | 1370 |
| Longitude in Degrees | 99 | 99 | 99 | 99 | 99 | 99 | 99 |
| Hemisphere | West | West | West | West | West | West | West |
| Receive Polarization | H | H | V | V | H | V | H |
| Transmit Polarization | H | V | H | H | H | H | H |
| Offset | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Symbol Rate (Msps) | 30 | 15 | 30 | 30 | 30 | 30 | 30 |
| Modulation Type | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK |
| Viterbi Mode | 7/8 | 3/4 | 3/4 | 5/6 | 5/6 | 5/6 | 7/8 |
| Shadow States | OK, KS | OK, KS | OK, KS | OK, KS, MN, ND, WA, MT, ID | OK, KS | OK, KS | OK, KS |
| Date Available | Live | Live | Live | Live | Live | Live | Live |
| Isolation | 29 | 29 | 29 | 29 | 29 | 29 | 29 |
| ACP | 62 | 62 | 62 | 62 | 62 | 62 | 62 |
| Minimum Signal | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 |
| Framing Mode | HDLC | HDLC | HDLC | HDLC | HDLC | HDLC | HDLC |
| To find out how to check frequency go to HNS-24381 | Go To Top |  |

| Satellite | G3C |
| --- | --- |
| Transponder Name | 9K | 17K | 21K | 24K |
| Channel ID | 22 | 21 | 23 | 25 |
| Frequency in Mhz | 1120 | 1307 | 1360 | 1420 |
| Longitude in Degrees | 95 | 95 | 95 | 95 |
| Hemisphere | West | West | West | West |
| Receive Polarization | H | V | H | H |
| Transmit Polarization | H | H | H | H |
| Offset | 0 | 0 | 0 | 0 |
| Symbol Rate (Msps) | 21.5 | 30 | 21.5 | 21.5 |
| Modulation Type | QPSK | QPSK | QPSK | QPSK |
| Viterbi Mode | 3/4 | 3/4 | 5/6 | 7/8 |
| Shadow States | Montana, North Dakota & Puerto Rico | OK, KS | Montana, North Dakota & Puerto Rico | Montana, North Dakota & Puerto Rico |
| Date Available | Live | Live | Live | Live |
| Isolation | 30 | 30 | 30 | 30 |
| ACP | 64 | 64 | 64 | 60 |
| Minimum Signal | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 |
| Framing Mode | HDLC | HDLC | HDLC | HDLC |

| Satellite | G10R |
| --- | --- |
| Transponder Name | 16K |
| Channel ID | 24 |
| Frequency in Mhz | 1272 |
| Longitude in Degrees | 123 |
| Hemisphere | West |
| Receive Polarization | H |
| Transmit Polarization | V |
| Offset | 0 |
| Symbol Rate | 10 Msps |
| Modulation Type | QPSK |
| Viterbi Mode | 1/2 |
| Shadow States |  |
| Date Available | Live |
| Isolation | 26 |
| ACP | 52 |
| Minimum Signal | 31 |
| Framing Mode | HDLC |

| Satellite | Horizons1 |
| --- | --- |
| Transponder Name | 11K | 16K | 22K | 23K |
| Channel ID | 51 | 34 | 33 | 35 |
| Frequency in Mhz | 1170 | 1270 | 1390 | 1410 |
| Longitude in Degrees | 127 | 127 | 127 | 127 |
| Hemisphere | West | West | West | West |
| Receive Polarization | H | V | V | H |
| Transmit Polarization | H | H | H | H |
| Offset | 0 | 0 | 0 | 0 |
| Symbol Rate | 30 Msps | 30 Msps | 30 Msps | 30 Msps |
| Modulation Type | QPSK | QPSK | QPSK | QPSK |
| Viterbi Mode | 5/6 | 5/6 | 5/6 | 5/6 |
| Shadow States | PR |  |  | PR |
| Date Available | 3/2/2006 | 12/22/2004 | Live | 2/8/2005 |
| Isolation | 30 | 30 | 30 | 30 |
| ACP | 60 | 60 | 60 | 60 |
| Minimum Signal | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 |
| Framing Mode | HDLC | HDLC | HDLC | HDLC |

| Satellite | AMC9 |
| --- | --- |
| Transponder Name | 24K | 23K | 22K | 21K | 19K | 18K | 17K |
| Channel ID | 36 | 38 | 37 | 48 | 49 | 39 | 50 |
| Frequency in Mhz | 1430 | 1410 | 1390 | 1370 | 1330 | 1310 | 1290 |
| Longitude in Degrees | 83 | 83 | 83 | 83 | 83 | 83 | 83 |
| Hemisphere | W | W | W | W | W | W | W |
| Receive Polarization | V | H | V | H | H | V | H |
| Transmit Polarization | H | V | H | H | H | H | H |
| Offset | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Symbol Rate | 30 Msps | 30 Msps | 30 Msps | 30 Msps | 30 Msps | 30 Msps | 30 Msps |
| Modulation Type | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK | QPSK |
| Viterbi Mode | 5/6 | 7/8 | 7/8 | 7/8 | 7/8 | 7/8 | 7/8 |
| Shadow State | PR, VI | PR, VI | PR, VI | PR, VI | PR, VI | PR, VI | PR, VI |
| Date Available | 3/23/2005 | 6/16/2005 | 5/17/2005 | 12/13/2005 | 01/24/2006 | 7/27/2005 | 2/10/2006 |
| Isolation | 32 | 32 | 32 | 32 | 32 | 32 | 30 |
| ACP | 66 | 66 | 66 | 66 | 66 | 66 | 60 |
| Minimum Signal | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 | HNS-24420 |
| Framing Mode | HDLC | HDLC | HDLC | HDLC | HDLC | HDLC | HDLC |

| Satellite | G3C (G3R) |
| --- | --- |
| Transponder Name | 13K |
| Channel ID | 4 |
| Frequency in MHz | 1210 |
| Longitude in Degrees | 95 |
| Hemisphere | West |
| Receive Polarization | H |
| Offset | 0 |
| Symbol Rate | 20 Msps |
| Modulation Type | QPSK |
| Viterbi Mode | 2/3 |
| Shadow States |  |
| Date Available | Live |
| Isolation | N/A |
| ACP | 30 |
| Minimum Signal | 100 |
| Framing Mode | HDLC |

| Satellite | IA6 |
| --- | --- |
| Transponder Name | 4K |
| Channel ID | 52 |
| Frequency in MHz | 1046 |
| Longitude in Degrees | 93 |
| Hemisphere | W |
| Receive Polarization | H |
| Transmit Polarization | H |
| Offset | 0 |
| Symbol Rate (Msps) | 45 Msps |
| Modulation Type | QPSK |
| Viterbi Mode | 3/4 |
| Shadow States | NONE |
| Isolation | 30 |
| ACP | 60 |
| Minimum Signal | HNS-24420 |
| Framing Mode | HDLC |
| To find out how to check frequency, go to HNS-24381 |

| Satellite | IA6-2 |
| --- | --- |
| Transponder Name | 14K | 28K |
| Channel ID | 54 | 53 |
| Frequency in MHz | 1216.5 | 1433.5 |
| Longitude in Degrees | 93 | 93 |
| Hemisphere | W | W |
| Receive Polarization | H | H |
| Transmit Polarization | H | H |
| Offset | 0 | 0 |
| Symbol Rate (Msps) | 21.5 Msps | 21.5 Msps |
| Modulation Type plus Viterbi Mode | Min QPSK 2/3, 8 PSK 5/6, 3/4, 2/3, 3/5 Max 8 PSK 8/9 | Min QPSK 2/3, 8 PSK 5/6, 3/4, 2/3, 3/5 Max 8 PSK 8/9 |
| Shadow States | NONE | NONE |
| Date Available | 8/22/2006 HN7000S Only | 7/24/2006 HN7000S Only |
| Isolation | 30 | 30 |
| ACP | 60 | 60 |
| Minimum Signal | HNS-24420 | HNS-24420 |
| Framing Mode | DVBS2 | DVBS2 |
| To find out how to check frequency, go to HNS-24381 NOTE: THIS IS A NEW SUPERPOD, NOT PART OF 52. |