|  | Home Networking with the DW7000 |
| --- | --- |
| Home Networking with the DW7000 Print The following article gives the basic steps needed to set up a home network with a HughesNet DW6000/7000. Note: Before you begin please print this article and the following "helper" articles in case you loose Internet connectivity: Configuring your browser to work with the DW6000/7000 proxy, Troubleshoot your connection to the DW6000/7000, Determine the network type of your DW6000/7000, How to Configure Your Computer for DHCP, To make this installation easier deal with only one computer first. Disconnect your computer from any network devices such as a router or hub. If you haven't done so already, connect your computer directly to the DW6000/7000. At this point you should be dealing with only one computer and it should be connected directly to the DW6000/7000. Browse to 192.168.0.1 . Do you see the DW6000/7000 Control Panel? If you do, go to the next step. If you don't, try one or both of the following: Configuring your browser to work with the DW6000/7000 proxy. Troubleshoot your connection to the DW6000/7000. Determine the network type of your DW6000/7000. Once you have determined how your DW6000/7000 is configured, click on one of the links below to see the specifics that pertain to your particular DW6000/7000 setup. DW6000/7000 with Network Address Translation (NAT) Connect using a Hub Connect using a Wireless Access Point. Connect using a router (Hardwired or Wireless) DW6000/7000 with Static IP and DHCP disabled Note: You must use a router for this configuration DW6000/7000 with Static IP and DHCP enabled Note: You must use a router for this configuration DW6000/7000 with NAT using a Hub Plug the DW6000/7000 and all PCs into your hub. Note: Do NOT plug into the Uplink port. Also if any of your PCs has Internet Connection Sharing enabled you must uninstall or disable it now. Run the LAN Client Configuration Utility (LCCU) on each computer to ensure proper performance. For help with this Click Here. DW6000/7000 with NAT using a Wireless Access Point. Disconnect your computer from the DW6000/7000. You will reconnect it to the network later. Establish communication between your PC and your wireless access point. If you are having trouble doing this please contact the manufacture of your access point. If your Access Point has a built in DHCP server you will need to disable. On the Access Point, you will need to disable the DHCP server and set the Access Point to obtain its IP address to automatically or dyanmically. Consult the owner's manual for instructions on how to do this. Note: For most Access Points these will be the default settings and no changes will be needed. Plug your DW6000/7000 into the wireless access point. Reboot your computer to renew its IP address. Establish communication between the rest of your computers and your Access Point. If you are having trouble doing this please contact the manufacture or your Access Point. To ensure proper performance, run the LAN Client Configuration Utility (LCCU) on each PC connected to the DW6000/7000. For help with this Click Here DW6000/7000 NAT router Note: A router is not the best choice for this type of network. A better choice would be a hard wired hub or a wireless access point. If you have no choice but to use a router follow the steps below to set it up to work with your network. Disconnect your computer from the DW6000/7000. You will reconnect it to the network later. Establish communication between your PC and your router. If you are having trouble doing this please contact the manufacture or your router. Note: Do NOT plug into the "WAN / Internet" port on your router. On the router, you will need to make the following changes to the LAN settings or setup. Consult the owner's manual for instructions on how to do this. Disable the built in DHCP server. Set its LAN IP address to 192.168.0.254. Set its LAN Subnet Mask to 255.255.255.0. Set its LAN Default Gateway to 192.168.0.1. Note: Not all routers will have these settings. If yours does not you should consider purchasing either a hard wired hub or a wireless access point. Also you may loose connectivity to your router after making these changes. If at any point you want to reset your router, most routers have a reset button on the back. Press and hold the reset button for at least 15 seconds. This will reset the router to its original factory settings and allow you to regain connectivity to it. Plug the DW6000/7000 into your router. Note: Do NOT plug into the "WAN / Internet" port on your router. Reboot your computer to renew its IP address. At this point you should have internet connectivity. If you don't recheck each step carefully. You can also try resetting your router's settings and starting over. Most routers include a reset button on the back for this purpose. Press and hold the reset button for at least 15 seconds. To ensure proper performance, run the LAN Client Configuration Utility (LCCU) on each PC connected to the DW6000/7000. For help with this Click Here This concludes the network setup. Anytime you want to access the router's internal webpage browse to 192.168.0.254. Anytime you want to access the DW6000/7000's internal web page browse to 192.168.0.1 DW6000/7000 Static IP with DHCP disabled Note: You will need a router for this configuration. If you haven't done so already obtain the IP address of your DW6000/7000. For help with this see Determine the network type of your DW6000/7000 Method 2. Configure your computer to obtain an IP address automatically. For help with this see How to Configure Your Computer for DHCP Disconnect the DW6000/7000 from your computer. You will reconnect it to the network later. Connect your computer to your router. Note: Do not plug your computer into, the port labeled "WAN / Internet". Establish communication between the router and your computer. If you are having trouble doing this please contact the manufacture or your router. Locate the WAN/Internet settings or setup section of your router. You will need to make some changes to these settings manually. Please consult your owner's manual for how to perform these settings if you are unfamiliar with how to do so. Note: Keep record of these settings you may need them later. Also you may loose connectivity to your router after making these changes. If at any point you want to reset your router, most routers have a reset button on the back for this purpose. Press and hold the reset button for at least 15 seconds. This will reset the router to factory settings and allow you to regain connectivity to your router. Set the WAN/Internet IP address to 1 greater than the DW6000/7000's IP address. For example, if the DW6000/7000 has an IP address or 67.189.135.66, you would set the router to 67.189.135.67. Set the WAN/Internet Subnet Mask to the same subnet mask as the DW6000/7000. For example if the DW6000/7000 has a subnet mask of 255.255.255.252 you would set the router's subnet mask to 255.255.255.252. Enter the IP address of the DW6000/7000 as the WAN/Internet Default Gateway. Set the WAN/Internet DNS server addresses to 66.82.4.8 & 66.82.4.12. Under the LAN setup or settings select Use Router as a DHCP server or Enable DHCP Server. Note: The specific wording on your router may vary. Plug the DW6000/7000 into the port labeled "WAN / Internet" on the router. At this point you should have internet connectivity. If you don't recheck each step carefully. You can also try resetting your router settings and starting over. Most routers include a reset button on the back for this purpose. Press and hold the reset button for at least 15 seconds. This will reset the router to factory settings and allow you to regain connectivity to your router. To ensure proper performance, run the LAN Client Configuration Utility (LCCU) on each PC connected to the DW6000/7000. For help with this Click Here. This concludes the network setup. Anytime you want to access the router's internal webpage browse to 192.168.0.1. Anytime you want to access the DW6000/7000's internal web page browse to the IP address you assigned it. In this example you would use 67.189.135.67 (yours will differ.) DW6000/7000 with Static IP and DHCP enabled Note: You will need a router for this configuration. If you haven't done so already obtain the IP address of your DW6000/7000. For help with this see Determine the network type of your DW6000/7000 Method 2. Disconnect the DW6000/7000 from your computer. You will reconnect the DW6000/7000 to the network later. Connect your computer to your router. Note: Do not plug your computer into the port labeled " WAN / Internet". Establish communication between the router and your computer. If you are unable to establish communication, you may need to change its configuration but first try resetting your router. Most routers have a reset button on the back for this purpose. This will reset the router to factory settings and allow you to regain connectivity to your router. Press and hold the reset button for at least 15 seconds. If you are still not able to communicate with your router you will need to make the following changes manually. If you are having trouble making these changes please contact the manufacture or your router. Under WAN setup or settings select obtain an IP address automatically or dynamically from ISP. Note: The specific wording on your router may vary. Under the LAN setup or settings select Use Router as a DHCP server or Enable DHCP Server. Note: The specific wording on your router may vary. Plug the DW6000/7000 into the port labeled "WAN / Internet" on the router. Wait a few minutes and check the WAN IP address of the router. It should change to a new address given to it by the DW6000/7000. This address should look very similar to the address of the DW6000/7000. For example if the DW6000/7000 has an IP address of 67.189.135.66 the router may have 67.189.135.67 or something similar (your will vary.) If the IP address of the router did not change try unplugging the router from the wall socket, waiting for 10 seconds, and plugging it back in this will reboot the router without undoing the changes you made its settings. If there is still no change check to see if the DW6000/7000 is plugged into the WAN/Internet port. Also, recheck the steps you have completed carefully. Once successful, write down the WAN IP address settings it received after rebooting. At this point you should have internet connectivity. If you don't recheck each step carefully. You can also try resetting your router settings and starting over. Most routers include a reset button on the back for this purpose. Press and hold the reset button for at least 15 seconds. This will reset the router to factory settings and allow you to regain connectivity to your router. To ensure proper performance, run the LAN Client Configuration Utility (LCCU) on each PC connected to the DW6000/7000. For help with this Click Here. Anytime you want to access the DW6000/7000's internal web page browse to 192.168.0.1. Anytime you want to view the router's internal web page browse to its WAN IP address. |